## Slide 1
Cyber Operation and Penetration Testing Scanning Cliff Zou University of Central Florida

## Slide 2: Acknowledgement
Content from the book:
“The Basics of Hacking and Penetration Testing: Ethical Hacking and Penetration Testing Made Easy”, Second Edition

## Slide 3: Acknowledgement
Presentation slides:
“Using Nessus and Nmap to Audit Large Networks”
By Greg Johnson, Principal Security Analyst University of Missouri – Columbia
  https://www.cs.uaf.edu/2003/fall/cs493/refs/JohnsonAudit.ppt

## Slide 4: Checking Machine Online Status?
root@kali: ping IPaddress
Windows with firewall enabled blocks PING by default for not home network (subnet)
Enable PING response in Windows:
  Search “firewall”, click “Windows Firewall” in control panel
  Click “Advanced settings” on the left
  From the left panel, click “Inbound Rules”
  Find the rules titled “File and Printer Sharing (Echo Request - ICMPv4-In)”
  Right-click each rule and choose “Enable Rule”.

## Slide 5: Ping and Ping Sweep
Ping Sweep: series of pings sent to a range of IP addresses
Tool: fping (preinstalled in Kali Linux)
fping -a -r 0 -g 192.168.0.1 192.168.0.254
  -a: only show live
  -r 0: retry ping number (0 means only 1 ping per IP)
  -g: the IP range
Con: only can find computers that respond to ICMP echo request message

## Slide 6: Port Scanning
Discover what services are running on a target computer
See the “common port number” sheet: http://packetlife.net/media/library/23/common_ports.pdf

## Slide 7: Pre-Knowledge: Network Layered Structure
What is the Internet?
Application
Application
Network
Network
Data Link
Transport
Transport
Data Link
Physical link
Web, Email, VOIP
TCP, UDP
IP
Ethernet, cellular

## Slide 8: Pre-Knowledge: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 9: TCP Connection Setup --- Three-Way Handshaking
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYN/ACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYN/ACK, replies with ACK segment, which may contain data
client
SYN,
seq=client_seq
server
SYN/ACK,
seq=server_seq, ack=client_seq+1
ACK,
seq=client_seq+1
ack=server_seq+1

## Slide 10: TCP Connection Management (cont.)
Closing a connection:
close();
Step 1: client end system sends TCP/FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 11: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed
Some applications simply send RST to terminate TCP connections immediately

## Slide 12: Private IP subnets used in NAT
10.0.0.0/8
  UCF using this large subnet
  Many global IPs  this 224 IP space
192.168.0.0/16
  Home WiFi and Wifi hotspot use this subnet
    Home Wifi uses 192.168.0.0/24, or 192.168.1.0/24
    Single global IP  this 256 IP space
172.16.0.0/12
  Not widely used

## Slide 13: TCP based Scan
TCP connect scan
  Open port: syn/ack response
  Closed port: rst/ack response
TCP syn scan (half-open scan)
TCP fin scan
TCP null scan (no flag is set)
TCP ack scan
TCP XMAS tree scan (all flags are set)

## Slide 14: Background: Port Status
A port can be:
Closed (not in use),
Open (listening), or
Filtered (the client computer asked for open or closed status report, and the target computer did not reply, usually due to a firewall.)

## Slide 15: Port Scanning Tool: Nmap
Included in Kali Linux
nmap –sT 192.168.0.101
  Default scan will scan 1000 TCP ports
For safety, try nmap on your own VMs in the same LAN, such as the Metasploitable VM

## Slide 16: Nmap Command Options
-sT: TCP connect scan
-sS: TCP SYN scan
-sA: TCP ACK scan
-sF: TCP FIN scan
-sX: XMAS tree scan
-sN: NULL scan
-sP: Ping scan
-sU: UDP scan
-sO: protocol scan
A good online tutorial:
  https://hackertarget.com/nmap-cheatsheet-a-quick-reference-guide/

## Slide 17: Nmap Target Selection
Scan a single IP
  nmap 192.168.1.1
Scan a host
  nmap www.testhostname.com
Scan a range of IPs
  nmap 192.168.1.1-20
Scan a subnet
  nmap 192.168.1.0/24
Scan targets from a text file
  nmap -iL list-of-ips.txt (one IP per line)

## Slide 18: Nmap Port Selection
Scan a single Port
  nmap -p 22 192.168.1.1
Scan a range of ports
  nmap -p 1-100 192.168.1.1
Scan 100 most common ports (Fast)
  nmap -F 192.168.1.1
Scan all 65535 ports
  nmap -p- 192.168.1.1
  Be careful with this. Generate large amount of scanning traffic!

## Slide 19: Nmap Port Scan Types
Scan using TCP connect
  nmap -sT 192.168.1.1
Scan using TCP SYN scan (default)
  nmap -sS 192.168.1.1
Scan UDP ports
  nmap -sU -p 123,161,162 192.168.1.1
Scan selected ports - ignore discovery
  nmap -Pn -F 192.168.1.1

## Slide 20: What NMAP Does Not Do
NMAP does not determine what program is running at an open port! Whatever service NMAP reports—http, ftp, smtp, etc.—is an assumption based on standards.
  Hacker trick: disguise a remote control access with the port number normally used by domain name service (53), web service (80), etc. especially if firewalls pass traffic on these ports.

## Slide 21: Service and OS Detection
Detect OS and Services
  nmap -A 192.168.1.1
  Will setup connection successfully and get the first data packet from the server
Standard service detection
  nmap -sV 192.168.1.1
More aggressive Service Detection
  nmap -sV --version-intensity 5 192.168.1.1
Lighter banner grabbing detection
  nmap -sV --version-intensity 0 192.168.1.1

## Slide 22: Service and OS Detection
The more aggressive service detection is often helpful if there are services running on unusual ports.
The lighter version of the service will be much faster as it does not really attempt to detect the service by simply grabbing the banner of the open service.

## Slide 23: Nmap Script Engine (NSE)
Nmap --script banner 192.168.0.101
  Setup TCP connection, get the first response text from the target
Nmap --script vuln 192.168.0.101
  Run a series of scripts looking for known vulnerabilities

## Slide 24: GUI-based Nmap: Zenmap
Included in Kali Linux
Where?
  Application menu  “Information Gathering…”  Zenmap
You can download Zenmap for Windows and Mac OS as well
  https://nmap.org/zenmap/

## Slide 25: Nessus: a GUI-based Power Network Scanner
Nessus is a proprietary vulnerability scanner which is developed by Tenable Network Security. It is free of charge for personal use in a non-enterprise environment ----wikipiedia.com
Download home-only FREE version: http://www.tenable.com/products/nessus/select-your-operating-system
Request a home-only registration key: http://www.tenable.com/products/nessus-home
Tutorial on installing nessus on Kali Linux
  http://www.tenable.com/blog/installing-and-using-nessus-on-kali-linux

## Slide 26: Install Nessus on Kali Linux
Download the free home version of nessus for Linux:
  Debian 6 and 7 / Kali Linux 1 AMD64 (64bit VM)
    File: Nessus-6.5.6-debian6_amd64.deb
  Debian 6 and 7 / Kali Linux 1 i386 (32-bit VM)
    File: Nessus-6.5.6-debian6_i386.deb

## Slide 27: Install Nessus on Kali Linux
    #dpkg –i Nessus-6.5.6-debian6_amd64.deb
      For programs existed in Kali’s App store, use “apt-get install …” to install them
    Enable nessus service first:
      #/etc/init.d/nessusd start
      Then the nessus demon will start to run
    Nessus relies on Web Browser for GUI and remote access
      Local access: https://localhost:8834/
      Remote access: https://192.168.0.3:8834/ (if the machine running nessusd has IP of 192.168.0.3)

## Slide 28: Web Browser-based GUI and Remote Access
Many recent software use this way for implementation
Pros:
  A user can remote access and use the software
  Remote user does not need any client-side software installation
Cons:
  Rely on the graphic and interaction functions provided by Browsers, may not be beautiful
  Could suffer the same Web-based attacks

## Slide 29: Use of Nessus
    Why Nessus runs as a webserver (on port 8834)?
      It enables other computers to do nessus scanning, too, by remote login to the Nessus server machine
    You can install Nessus server on Linux, or Windows
    Nice video tutorial on using Nessus:
      https://www.youtube.com/watch?v=r_pDVhNoYr0

## Slide 30: Use of Nessus
Assume the Nessus is installed in Kali VM
We run Nessus on the Win7 VM in the same LAN
  The warning is normal
  Due to the Nessus
  Server has no valid
  Digital certificate

## Slide 31: Use of Nessus
First run, set up an account as you choose the username and password

## Slide 32: Use of Nessus
First run, after account set up, you need to input your activation code:

## Slide 33: Use of Nessus

## Slide 34: Use of Nessus
The free version comes with a few predefined types of scans
  The gray entries are only available in commercial version

## Slide 35: Use of Nessus
Test of Basic Network Scan:
  You can test to scan your Kali VM, Win7 VM,
  The best target is the Metasploitable VM since it has many vulnerabilities that can be discovered by Nessus

## Slide 36
Metasploitable 2 Virtual Machine
Use nmap to see what services are running on this Linux
Use Nessus installed on your Kali Linux to check any known vulnerabilities on this Linux

## Slide 37: Is Scanning Dangerous?
Both NMAP and NESSUS aim to never damage data.
In MU’s NMAP and NESSUS scanning of 13,000 connections in its network, no data has ever been lost through scanning.

## Slide 38: Is Scanning Dangerous?
HOWEVER!
NMAP and especially NESSUS can freeze scanning targets. The network application may freeze. The entire system may require restarting. Some devices such as printers or routers may reset themselves—or not.

## Slide 39: Is Scanning Dangerous?
In MU’s scanning, freezes are rare: about one in six hundred general purpose systems for tests that are not explicitly dangerous.
NESSUS designates about 10% of its tests as dangerous, denial of service attacks such as oversize data or flooding. In tests of 200 diverse systems, around one third eventually fell to a denial of service attack.

## Slide 40: Is Scanning Dangerous?
A full 65,535 TCP port scan and service check generates
  at least 5 MB of traffic to the target
  and at least 6 MB in reply.
  Most of this traffic is small packets.
Hence…

## Slide 41: Is Scanning Dangerous?
Typical testing over a 10 or 100 Mbps connection will noticeably but not painfully slow target system performance for around 15 minutes.
Scanning multiple targets through one network device can slow that subnet’s performance.
NMAP and NESSUS offer options to scan slowly or aggressively, and to randomize target sequence.

## Slide 42: Safe Scans
Hence, scan critical infrastructure systems with someone ready to restart systems. Performance monitoring may yield insights.
For extra safety, move NESSUS denial of service tests out of their normal directory.